## Slide 1: ADS-B
REFLECTIONS ON 2018 INSTALLATIONS

## Slide 2: WHAT IS ADS-B?
Automatic Dependent Surveillance - Broadcast
  ADS-B is a system in which electronic equipment onboard an aircraft automatically broadcasts the precise location of the aircraft via a digital data link. Other aircraft and ATC can see the aircraft’s position/altitude without the need for radar
ADS-B Operating Frequencies
  1090 MHz – associated with current Mode A, C, and S transponders. ADS-B info included within Mode S Extended Squitter (ES) messages
  978 MHz – Universal Access Transceivers (UAT). US only
ADS-B Out - Transmission of ADS-B information from an aircraft
ADS-B In - Receipt of ADS-B information by an aircraft
Different equipment required for Out vs In capabilities
FAA 1/1/2020 Mandate addresses ADS-B Out usage
Also
  ADS-R – Translation, reformatting, and rebroadcasting information to enable aircraft operating on an alternate frequency to process other aircraft’s information
  TIS-B – Broadcast of transponder-based traffic information derived from ATC surveillance systems
  FIS-B – UAT only. Advisory aeronautical and weather information

## Slide 3: ADS-B Airspace

## Slide 4: WHY INSTALL ADS-B OUT?
Gliders are exempt aren’t they?
  The regulation 14 CFR 91.225(e) allows aircraft not certificated with an electrical system, including balloons and gliders, not equipped with ADS-B Out to operate within 30 nautical miles of a Class B primary airport—basically, within its Mode C veil—while remaining outside of any Class B or Class C airspace.
  These aircraft can operate as high as 17,999 feet msl except above Class B or Class C airspace; they also can operate beneath Class B and Class C airspace.
  Operationally the ADS-B Out rules mirror the transponder equipage requirements in 14 CFR 91.215.
Relevant denied airspace without ATC approval
  Above Class B & C and less than 10,000’
  Spokane/Fairchild AFB 6400’ to 10,000’
“See and avoid”
  Is becoming “See, be seen, and avoid”

## Slide 5: WHAT TYPE OF ADS-B?
Full compliance – TSO-C166b (or TSO-C154c), 91.227
  Source Integrity Level (SIL)=3
    Experimental, TT22, TN72, GPS Antenna
    Certified, TT22, TN70, TA70 GPS Antenna, w/advisory 337
TABS (Traffic Awareness Beacon System) – TSO-C199
  Visible to other aircraft with TAS, TCAS I, TCAS II, and ADS-B IN
  SIL=1
    TT21, TN72, GPS Antenna
Other
  SIL=0
    TT?? With GPS via NMEA from PowerFLARM

## Slide 6: N317KF (Experimental) Installation
Previously installed Trig TT22 Mode S Transponder
Added
  Trig TN72 GPS Receiver (~$375)
  GPS Active Antenna (~$50)
  Peregrine Squat Airspeed Switch Kit (~$125)
    w/STC, cheaper as a part for Experimental
Upgraded
  Trig TT22 upgraded to the latest software

## Slide 7: Assessing ADS-B OUT Performance
FAA Public ADS-B Performance Report
  https://adsbperformance.faa.gov/paprrequest.aspx (or Google)
  Full ADS-B compliance testing only

## Slide 8: First FLIght
Williams, CA
Comparing SeeYou and FAA
  Take off
    SeeYou 20:53:11,
    FAA 20:53:44 (~50’ AGL)
  Landing
    SeeYou 21:41:05
    FAA 21:40:48
Squat switch changed GND -> ALT mode ~40kts

## Slide 10: More Acronyms
NIC – Navigation Integrity Category
  Radius of containment around the aircraft.
  91.227 requires a min NIC of 7 (<370m)
SIL – Source Integrity Level
  Measure of the probability of not being within the containment radius without indication
  91.277 requires a value of 3 (prob exceeding NIC < 1 x 10-7 / flight hour)
NACp – Navigation Accuracy Category for Position
  Accuracy of the aircraft position being transmitted
  91.277 requires a min NACp of 8 (95% Horz accuracy bounds < 92.6m)
NACv – Navigation Accuracy Category for Velocity
  1 = < 10 m/s
SDA – System Design Assurance
  Likelihood of bad data being sent
  Pass values of 2 or 3 (prob false/misleading info < 1 x 10-5 / flight hour)

## Slide 11: Resolving Performance Issues
Working hypothesis was that the GPS wasn’t getting an accurate enough fix
Placement of GPS Antenna variations
  Original location deep in instrument bay on one side
    % Failure rate : NIC = 7.68% (FAIL), NACp = 1.63% (pass), other 0.0%
    High banked turns causing too much other equipment to get in the way?
  Second attempt (3/31)
    GPS Antenna relocated high and central
    Level flight, all other GPS antennas disconnected during short flight
    % Failure rate : NIC = 59.07% (FAIL), NACp = 12.46% (FAIL), other 0.0%
    Too close to active FLARM antenna

## Slide 12: Resolving Performance Issues
Placement of GPS Antenna (cont.)
  Third attempt (4/1)
    FLARM off, all other systems on, short level flight
    % Failure rate : 0.0% on all metrics – Complete PASS
  Fourth attempt (4/2)
    As above but normal gliding maneuvers
    % Failure rate : NIC = 1.19% (pass), NACp = 0.12% (pass), other 0.0%
  Fifth attempt (4/22)
    Relocated GPS Antenna onto canopy ledge by right elbow
    Loooong connecting cable
    All equipment turned on, normal gliding maneuvers
    % Failure rate : 0.0% on all metrics – Complete PASS
Could have done attempts 1 thru 4 on the same day but wasn’t certain how to drive the FAA website
Have checked six other flights since – still getting pass marks

## Slide 13: “Be seen”
Numerous reports of being able to be seen for miles
Flightaware ADS-B tracking in real-time
  https://flightaware.com/live/flight/N317KF

## Slide 14: Still getting “close encounters”
Boeing 787 Flight Test 5/13
  Above Ephrata township
    787 was descending, I was climbing. Past within ¼ mile and 1000’ vertical separation
    Flight Nav computer had zoomed in while thermalling (so no PowerFLARM derived ADS-B situational awareness)
    No ADS-B IN display
BAe 146 Fire fighting air tankers
  Above Mackay, ID below cloudbase
  Transitioning Ephrata/Grant County
  No electronic position transmission
  Mark I eye-ball

## Slide 15: So what’s next? - ADS-B IN
iLevil AW 2
  Dual band (1090/978 MHz) receiver
  ADS-B, ADS-R, TIS-B, FIS-B, AHRS, RS-232
Outputs GDL-90 and proprietary messages via WiFi
3rd Party Apps (typically running on Tablets)
  ForeFlight, Xavion, Naviator, Sky-Map, etc
Or home-grown application
  Emphasis on collision avoidance not merely situational awareness that requires constant monitoring
And you thought FLARM leaching was bad…

## Slide 16
QUESTIONS?